 G3 Protocol (FW v 4.02 & newer)
Overview
Where to find implementations of this protocol
Firmware
Host software
Network Overview
Packet Protocol
Protocol Overview
Timeouts
Handling Packet Failures
Command Buffering
Packet structure
Command structure
Host Commands
Slave Commands
Slave IDs
Response Packets
Response Packet Payload Structure
Test Commands
0x70 - Echo test
0x71 - Generate bad response packet
0x72 - Simulate bad packet reception
0x73 - Passthru to slave
0x74 - Clear command queue
0x75 - "NO SUCH COMMAND" command
0x76 - Set Debug Code
0x77 - Get Debug Code
0x78 - Get Debug Buffer
0xF0 - Command queue filler
Master Microcontroller Commands (3-axis controller)
Query Commands
0 - Get Version - Query firmware for version information
1 - Init - Initialize firmware to boot state
2 - Get Available Buffer Size - Determine how much free memory we have for buffering.
3 - Clear Buffer - Empty the command buffer
4 - Get Position - Get the current position of the tool
6 - Set Range - Set the maximum range of travel on all axes. - OBSOLETE
7 - Abort Immediately - Stop Machine, Shut Down Job Permanently
8 - Pause / Unpause - Halt Execution Temporarily
9 - Probe - Move in Z axis (negative) until probe hits something
10 - Tool Query - Query a tool for information
11 - Is Finished - See if the machine is currently doing anything
12 - Read from EEPROM
13 - Write to EEPROM
14 - Capture to file
15 - End capture
16 - Playback capture
17 - Reset
18 - Get next filename
19 - Read debug registers
20 - Get firmware build name
21 - Get Extended Position - Get the current position on 5 axes
22 - Extended Stop - Stop subset of systems
23 - Get Motherboard Status
24 - Build Start Notification
25 - Build End Notification
26 - Get communication statistics
Buffered Commands
128 - RESERVED (Obsolete command)
129 - Queue point
130 - Set Position
131 - Find Axes Minimums - Blocking seek to hardware min switches, w/ timeout
132 - Find Axes Maximums - Blocking seek to hardware max switches w/ timeout
133 - Delay - Simply stop and wait.
134 - Change Tool - Switch to a new tool
135 - Wait For Tool Ready - Wait until a tool is ready before proceeding
136 - Tool Action Command - Send an action command to a tool for execution
137 - Enable/Disable Axes - Explicitly power or depower steppers
138 - User Block
139 - Queue extended point
140 - Set Extended Position
141 - Wait For Platform Ready - Wait until the build platform is ready before proceeding
142 - Queue extended point, new style
143 - Store Home Positions
144 - Recall Home Positions
Slave Microcontroller Commands (Extruder)
Query Commands
0 - Get Version
1 - Init - Initialize firmware to boot state
2 - Get Temperature
3 - Set Target Temperature
4 - Set Motor 1 Speed (PWM)
5 - Set Motor 2 Speed (PWM)
6 - Set Motor 1 Speed (RPM)
7 - Set Motor 2 Speed (RPM)
8 - Set Motor 1 Direction
9 - Set Motor 2 Direction
10 - Toggle Motor 1 (on/off)
11 - Toggle Motor 2 (on/off)
12 - Toggle Fan (on/off)
13 - Toggle Valve (on/off)
14 - Set Servo 1 Position
15 - Set Servo 2 Position
16 - Filament Status
17 - Get Motor 1 Speed (RPM)
18 - Get Motor 2 Speed (RPM)
19 - Get Motor 1 Speed (PWM)
20 - Get Motor 2 Speed (PWM)
21 - Select Tool
22 - Is Tool Ready?
23 - Pause/Unpause - Halt Execution Temporarily
24 - Abort - Terminate all operations and reset
25 - Read from EEPROM
26 - Write to EEPROM
30 - Get Build Platform Temperature
31 - Set Build Platform Target Temperature
32 - Get Extruder Target Temperature
33 - Get Build Platform Target Temperature
34 - Get firmware build name
35 - Is Build Platform Ready?
36 - Get Tool Status
37 - Get PID state
38 - Set Motor 1 Speed (DDA)
39 - Set Motor 2 Speed (DDA)
40 - Light indicator LED
Changes and additions to the protocol
Errata

# Overview
This document describes the protocol by which 3rd and 4th generation RepRap electronics communicate with their host machine, as well as the protocol by which the RepRap host communicates with its subsystems.  The same simple packet protocol is used for both purposes.

# Where to find implementations of this protocol
# Firmware
The default firmware for the default generation 3 electronics can be found on GitHub at http://github.com/makerbot/G3Firmware.

# Host software
Currently the only software suite implementing this protocol is ReplicatorG.  It can be found on GitHub at http://github.com/makerbot/ReplicatorG.

# Network Overview
The RepRap Generation 3 electronics set consists of several hardware components:
1. A single Master Controller which controls the 3-axis steppers, communicates with a host PC, supports a storage card and controls a set of toolheads.
2. A set of Stepper Drivers which drive the steppers based on signals from the master controller.  The communications between the drivers and the master controller is outside of the scope of this document.
3. A number of Tool Controllers which control extruders, cutters, frostruders, etc.

The two communications channels covered by this document are:
1. The Host Network, between a host computer and the master controller
2. The Slave Network, between the master controller and one or more tool controllers.

The host network is generally implemented over a standard TTL-level RS232 serial ion.  The slave network is implemented as an RS485 serial bus driven by SN75176A transceivers.

# Packet Protocol
# Protocol Overview
Each network has a single master: in the case of the host network, this is the host computer, and in the case of the slave network, this is the master controller.  All network communications are initiated by the network master; a slave node can never initiate a data transfer.

Data is sent over the network as a series of simple packets.  Packets are variable-length, with a maximum payload size of 32 bytes.

Each network transaction consists of at least two packets: a master packet, followed by a response packet.  Every packet from a master must be responded to.

Commands will be sent in packets. All commands are query/response.  The master in each pair will always initiate communications, never the slave.  All packets are synchronous; they will wait for a response from the client before sending the next packet.  The firmware will continue rendering buffered commands while receiving new commands and replying to them.

# Timeouts
Packets must be responded to promptly.  No command should ever block.  If a query would require more than the timeout period to respond to, it must be recast as a poll-driven operation.

All communications, both host-mb and mb-toolboard, are at 38400bps.  It should take approximately 1/3rd ms. to transmit one byte at those speeds.  The maximum packet size of 32+3 bytes should take no more than 12ms to transmit.  We establish a 20ms. window from the reception of a start byte until packet completion.  If a packet is not completed within this window, it is considered to have timed out.

It is expected that there will be a lag between the completion of a command packet and the beginning of a response packet.  This may include a round-trip request to a toolhead, for example.  This window is expected to be 36ms. at the most.  Again, if the first byte of the response packet is not received by the time 36ms. has passed, the packet is presumed to have timed out.

# Handling Packet Failures
If a packet has timed out, the host or board should treat the entire packet transaction as void.  It should:
- Return its packet reception state machine to a ready state.
- Presume that no action has been taken on the transaction
- Attempt to resend the packet, if it was a host packet.

# Command Buffering
To ensure smooth motion, as well as to support print queueing, we'll want certain commands to be queued in a buffer.  This means we won't get immediate feedback from any queued command.  To this end we will break commands down into two categories: action commands that are put in the command buffer, and query commands that require an immediate response.  In order to make it simple to differentiate the commands on the firmware side, we will break them up into two sets: commands numbered 0-127 will be query commands, and commands numbered 128-255 will be action commands to be put into the buffer.  The firmware can then simply look at the highest bit to determine which type of packet it is.

Every packet gets precisely one response packet.  Query commands must be sent in their own packet.  Only action or query commands can be sent in a single packet.  The first byte of the command payload will determine the nature of the entire packet.  Thus, you cannot mix query and action commands in a single packet!

Command Types

Range	Type	Description
0-127	Query Commands	Commands that can be executed immediately, and thus do not need to be queued. Generally return pre-calculated information and should be fast.
128-255	Action Commands	Commands that must be executed one at a time, and in a particular order. These commands should be buffered for smooth operation. Many of there commands may take up a large amount of time to complete.

# Packet structure
Command packets are sent from the Master to the Slave.  This can either be from the Host CPU to the Master uC or from the Master uC to the Slave uC.  It consists of a two-byte header, a variable-length payload, and a 1 byte CRC footer.

The packet consists of:

Index	Name	Details
0	Start byte	This byte always has the value 0xD5 and is used to ensure synchronization.
1	Length	This byte indicates the length of the payload (excluding the header and CRC) in bytes.
2...	Payload	The packet payload. This is appended to the buffer and either immediately executed and removed (if a query type) or buffered for execution (if an action type).
Length+2	CRC	This is the 8-bit iButton/Maxim CRC of the payload.

Command length is implicit in the command structure; no explicit separator is needed.

# Command structure

# Host Commands
The payload of a packet consists of one command.  Each command contains a header, as follows:

Index	Name	Details
0	Command	The command code to send to the device.
1-N	Arguments	Arguments to this command (details below as 'command payload').

# Slave Commands
The payload of a packet consists of one command.  Each command contains a header, as follows:

Index	Name	Details
0	Slave ID	The ID of the slave device being addressed. The value 127 represents any available device; see below. / New as of firmware version 2.92. Previously, 255.
1	Command	The command code to send to the device.
2-N	Arguments	Arguments to this command (details below as 'command payload').

# Slave IDs

The slave ID is the ID number of a toolhead.  A toolhead may only respond to commands that are directed at its ID.  If the packet is corrupt, the slave should *not* respond with an error message to avoid collisions.

The exception to this is the slave ID 127.  This represents any listening device.  The address 127 should only be used when setting the ID of a slave.
New as of firmware version 2.92. Previously, the broadcast address was 255.

# Response Packets
Response packets look just like command packets.  The only difference is the payload is guaranteed to contain a response code as the first byte, as described below.  The only exception is certain debugging packets, which will specifically indicate such in their description.
# Response Packet Payload Structure

Index	Name	Details
0	Response Code	This is a standard response code that is included with all packets and is described below.
1-N	Response Data	This contains response-specific data. Length is implicit based on the command being responded-to.

If the command was a non-request command, the response data is always empty.

Response Code Values
Note: These are changed starting in version 2.92. Previously, they were 0x0 - 0x7.

Response Code	Interpretation
0x80	Generic error, packet discarded.
0x81	Success.
0x82	Action buffer overflow, entire packet discarded.
0x83	CRC mismatch, packet discarded.
0x84	Query packet too big, packet discarded.
0x85	Command not supported/recognized.
0x86	Success; expect more packets. Used when a single reponse packet cannot contain the entire message to be retrieved.
0x87	Downstream timeout (for example, a toolhead timed out).

Data Formats

The protocol is a byte-oriented protocol.  Payloads may contain various information in a variety of formats, but will generally be limited to the formats described below.  Multi-byte datatypes will always be transmitted in Little-endian mode.  Remember, this means that the least significant byte ("littlest") byte is sent first!  For a more in-depth discussionof little-endian storage, see: http://en.wikipedia.org/wiki/Endianness#Little-endian

Various Data Types

Type	Range
uint8	0 to 255
uint16	0 to 65,535
int16	-32767 to 32,767
uint32	0 to 4,294,967,295
int32	-2,147,483,647 to 2,147,483,647

# Test Commands
The command codes of the form 0xFX and 0x7X are reserved for diagnostic test packets.  The firmware is not guaranteed to implement any of these operations.

# 0x70 - Echo test
This command indicates that the client should resend the original packet data, minus the echo test byte.  The client will not send a response code-- the remaining payload will be copied verbatim.  This will persuade the client to send any valid packet the host wants.

Payload: variable.
Response: resend of payload.

# 0x71 - Generate bad response packet
This command will request that the client respond with a test packet that exhibits the given error.
1	No response
2	Skip start byte
3	Bad packet length (specified length too long)
4	Bad/incorrect CRC
5	Start byte, then timeout

Payload: 1 byte.
    uint8: Error type to simulate.

# 0x72 - Simulate bad packet reception
This command will essentially instruct the recipient to behave as if the received packet had experienced the specified error.  The error codes are:
1	Received noise
2	Bad packet length (specified length too long)
3	Bad/incorrect CRC
4	Timeout

Payload: 1 byte.
    uint8: Error type to simulate.

# 0x73 - Passthru to slave

This command will pass the enclosed packet on to its slave bus, and return a copy of the returned packet if the packet receipt is successful.  If the packet receipt is unsuccessful (for example, if the packet times out) it should return a generic error.  The client will not send a response code if successful-- instead it will just mirror as much of the packet as possible.

Payload: N bytes.
    The payload of the packet to send to the slave bus.

Response: N bytes.
    Complete payload of response packet, truncated to fit if necessary.

# 0x74 - Clear command queue
This command will clear the command queue completely and immediately.

Payload: 0 bytes.
# 0x75 - "NO SUCH COMMAND" command
This command code has no definition, and is reserved an an unimplemented command for test purposes.

# 0x76 - Set Debug Code

This command sets the blink code for the target board.  Setting the code to '0' will turn off the debug code.

Payload: 2 bytes.
    uint8: the debug register to set.  Should always be '0'.
    uint8: the value to set the debug register to.  For register '0', the number of blinks to display.
    Response: 0 bytes.

# 0x77 - Get Debug Code
Retrieve the value of a debug register.  '0' is the debug register containing the blink code.  Other registers are undefined.

    Payload: 1 byte.
    uint8: the debug register to read.  Should always be '0'.
    Response: 1 byte.
    uint8: the value of the debug register.

# 0x78 - Get Debug Buffer
(only on the firmware_debug branch in github/makerbot:G3Firmware)
Retrieve the contents of the debug buffer and clears it.

    Response: N bytes.
        The current contents of the debug buffer, the data in the buffer is whatever the firmware puts in there.

# 0xF0 - Command queue filler
This is a nop command that will remain on the command queue until cleared.  It may specify padding bytes to help fill space on the buffer.

Payload: 1 + N byte.
    uint8: the number of padding bytes following this byte.  The total space on the command buffer will be 2+N.
    uint8 * N: padding bytes.  The actual values are ignored.

# Master Microcontroller Commands (3-axis controller)
# Query Commands
# 0 - Get Version - Query firmware for version information
    This command allows the host and firmware to exchange version numbers.  It also allows for simple automated discovery of the firmware.  Version numbers will always be stored as a single number, Arduino / Processing style.  Thus, the versions will be 0 to 65535.

Payload (2 bytes) - host version
   uint16: Host Version.

Response (2 bytes) - firmware version
    uint16: Firmware Version
# 1 - Init - Initialize firmware to boot state
    Initialization consists of:
  - resetting current position to 0,0,0
  - clearing command buffer
  - setting range to eeprom value (if it exists)  otherwise its 0.

    Payload (0 bytes)
    Response (0 bytes)
# 2 - Get Available Buffer Size - Determine how much free memory we have for buffering.
    This command will let us know how much buffer space we have available for action commands.  It can be used to determine if and when the buffer is available for writing.  If we are writing to the SD card, it will generally always report the maximum number of bytes available.

Payload (0 bytes)

    Response (4 bytes)
    uint32: number of bytes available in the command buffer.
# 3 - Clear Buffer - Empty the command buffer
    This command will empty our buffer, and reset all pointers, etc to the beginning of the buffer.  If writing to an SD card, it will reset the file pointer back to the beginning of the currently open file.  Obviously, it should halt all execution of action commands as well.

    Payload (0 bytes)
    Response (0 bytes)
# 4 - Get Position - Get the current position of the tool
    Useful for determining current position of the toolhead.  It is up to the host software to add or subtract the toolhead offset to determine the actual position of the toolhead.  It will also return the status of the various endstops for diagnostic information.

Payload (0 bytes)

Response (13 bytes)
    int32: current x position, in steps
int32: current y position, in steps
int32: current z position, in steps
    uint8: bits marked for endstop status: (7-0) : | N/A | N/A | z max | z min | y max | y min | x max | x min |

5 - Get Range - Get the maximum range of travel on all axes. - OBSOLETE
    When find axes maximums is called, it will record the maximum as the range.  internally, it will keep track of its range and this function will simply report that internal value. We cannot assume that there are endstop switches for all axes at both min and max positions. The firmware will know this, so the "Find Axes min/max" commands may be partially no-ops in this case. The firmware should always respect this range and never go beyond it.

    Payload (0 bytes)
    Response (12 bytes)
    uint32: x range, units in steps
uint32: y range, units in steps
    uint32: z range, units in steps
# 6 - Set Range - Set the maximum range of travel on all axes. - OBSOLETE
    This command tells the firmware what its maximum range of travel is.  The firmware should always respect this. This should be recorded into the eeprom for future usage.

    Payload (12 bytes)
    uint32: x range, units in steps
uint32: y range, units in steps
    uint32: z range, units in steps

    Response (0 bytes)
# 7 - Abort Immediately - Stop Machine, Shut Down Job Permanently
    This function is intended to be used to terminate a print during printing.  Extruder and accessories off, steppers disabled, everything shuts down.

Payload (0 bytes)
    Response (0 bytes)
# 8 - Pause / Unpause - Halt Execution Temporarily
    This function is intended to be called infrequently by the end-user in order to make build-time adjustments immediately and easily.  No buffers or other run-time variables are changed.  The pause command should also prompt the firmware to send a pause command to the toolhead.

    On pause, it stops all movement, stops extrusion, moves up a 'safe z' amount, and waits for new commands.
    On unpause, it lowers to original Z, optionally restarts extrusion, and resumes movement.
    agm: Currently we do not do the "safe Z" backoff.  I'd like to introduce that as a parameter instead.

    Payload (0 bytes)
    Response (0 bytes)
# 9 - Probe - Move in Z axis (negative) until probe hits something
    This command will wait until the buffer is clear to avoid conflicts.  It will also prevent any buffered commands from executing for the duration of the probe.

    Payload (6 bytes)
    uint32: feedrate (in microseconds between steps) (max 71.58 minutes)
    uint16: timeout (in seconds before abort)  (max = 18 hours) (default = 1 minute)

    Response (4 bytes)
    uint32: Z position when probe has been triggered.
# 10 - Tool Query - Query a tool for information
    This command is for sending a query to the tool.  The master firmware will then pass the query along to the appropriate tool, as well as passing the response back as well.  This allows the tool specific commands to be developed independently between.

    Payload (2 + N bytes)
    uint8: the index of the tool to query
    uint8: the query command for the tool.
    N bytes: command specific payload, variable size.

    Response (0-N bytes)
    0-N bytes: the command specific response, if any.
# 11 - Is Finished - See if the machine is currently doing anything
    This command lets us know if the machine is finished executing its current command queue.

Payload (0 bytes)

    Response (1 byte)
    uint8: 0 if still in progress; 1 if finished.
# 12 - Read from EEPROM
    Read the specified number of bytes from the given offset in the EEPROM and return it in the response packet.  The maximum read size is 32 bytes.

    Payload (3 bytes)
    uint16: the offset of the read
    uint8: the number of bytes to return, N.  N <= 16.

    Response (N bytes)
    N bytes: the data read from the EEPROM.
# 13 - Write to EEPROM
    Write the given bytes to the EEPROM starting at the specified location.  The maximum payload size is 16 bytes.

    Payload (3+N bytes)
    uint16: the offset of the write
    uint8: the length of the data
    N bytes: the data to write

    Response (1 byte)
    uint8: the number of bytes successfully written.
# 14 - Capture to file
Capture all subsequent commands up to the next "end capture" command to a file with the given name on the SD card.  The file will be stored in the root of the fat16 filesystem on the SD card.  The maximum file name length permitted is 12 characters, including the '.' and file name extension.  Welcome to the brave new world of MS-DOS 2.0!

    Payload (N bytes)
    N bytes: the name of the file in ascii, terminated with a null
    Response (1 byte)
    uint8: response code
- 0 if operation was successful
- 1 if no SD card was present
- 2 if SD card init failed
- 3 if partition table could not be read
- 4 if filesystem could not be opened
- 5 if root directory could not be opened
- 6 if SD card is locked
# 15 - End capture
    Complete an ongoing file capture.

    Payload (0 bytes)
    Response (4 bytes)
    uint32: the total size of the capture in bytes
# 16 - Playback capture
    Play back a file containing captured data to the makerbot.  The maximum file name length permitted is 12 characters, including the '.' and file name extension.  While the makerbot is in playback mode, it will only respond to pause, unpause, and stop commands.

    Payload (N bytes)
    N bytes: the name of the file in ascii, terminated with a null
    Response (1 byte)
    uint8: response code
0 if playback successfully initiated
- 1 if no SD card was present
- 2 if SD card init failed
- 3 if partition table could not be read
- 4 if filesystem could not be opened
- 5 if root directory could not be opened
- 7 if file was not found
# 17 - Reset
    Reset the board remotely.  Useful for reprogramming the board without having to fiddle with switches.  The board will reset immediately after sending the response.
    Payload (0 bytes)
    Response (0 bytes)
# 18 - Get next filename
    Retrieve the next valid filename from the SD card.  If a non-zero value is passed to the "restart" parameter, the file list will begin again from the start of the directory.  The file list state will be reset if any other SD operations are performed.
    Payload (1 byte)
    uint8: restart (0 to continue reading, 1 to begin anew)
    Response (N+1 bytes)
    uint8: an SD response code, one of the following:
0 if operation was successful
- 1 if no SD card was present
- 2 if SD card init failed
- 3 if partition table could not be read
- 4 if filesystem could not be opened
- 5 if root directory could not be opened
    N bytes: the name of the file in ascii, terminated with a null.  If the operation was unsuccessful, this will be the empty string.  Even if there was an SD card error, the null string should be returned.
# 19 - Read debug registers
    Retrieve the value in the specified debugging register.  These are essentially "scratch" registers for development.  All registers are 8-bit.
    0: number of CRC errors in extruder responses
    1: number of malformed packet responses from extruder
    2: number of timeouts on packet responses from extruder
    Payload (1 byte)
    uint8: index of debug register
    Response (1 byte)
    uint8: value of register

# 20 - Get firmware build name
    New in version 2.3
    Retrieve the firmware build name, which is a human-readable string describing the build.  Names should be chosen with an eye towards disambiguating builds targeted for different tools.
    Payload length limitations restrict this field to 31 characters.
    Payload (0 bytes)
    Response (N+1)
    char[N+1]: a null-terminated string representing the build name

# 21 - Get Extended Position - Get the current position on 5 axes
New in version 2.4
    Retrieve the current position of all axes that this machine supports.

Payload (0 bytes)

Response (22 bytes)
    int32[n]: position of axis n, in steps.
    int16: bits marked for endstop status: (A-0) : | b max | b min | a max | a min | z max | z min | y max | y min | x max | x min |

# 22 - Extended Stop - Stop subset of systems
New in version 2.7
    Stop the stepper motor motion or other subsystems.

Payload (1 byte)
    uint8: bitfield indicating which subsystems to shut down
    bit 0: halt all stepper motion immediately.
    bit 1: clear command queue.

Response (1 byte)
    int8: Result code.
- 0 if command terminated normally and subsystems were stopped.
- 1 for generic error (command failed).
# 23 - Get Motherboard Status
    Proposed for version 2.9
    Retrieve some information about the motherboard

    Payload (0 bytes)
    Response (1 byte)
       uint8: As below:

Bit	7	6	5	4	3	2	1	0
Name	POWER_ERROR	N/A	WDRF	BORF	EXTRF	PORF	N/A	N/A

POWER_ERROR - An error was detected with the system power. For Gen4 electronics, this means ATX_5V is not present.
WDRF - Watchdog reset flag was set at restart
BORF - Brown out reset flag was set at restart
EXTRF - External reset flag was set at restart
PORF - Power-on reset flag was set at restart

# 23 - Build Start Notification
    Implemented in 4.02, mighty board only
  Tells the motherboard that it is about to begin a build, and provides some information about the job for status reporting. The maximum file name length permitted is 12 characters, including the '.' and file name extension.
    Payload (4+N bytes)
    uint32: Set number of steps in the build
    N bytes: Length of name string (bytes)

# 24 - Build End Notification
    Implemented in 4.02, mighty board only
Tells the motherboard that the current build has ended.

    Payload (1 bytes)
    uint8: Reason for build end (uint8 cause. 0 is normal ending, 1 is user cancel, 0xFF is cancel due to error or safety cutoff)
# 25 - Get communication statistics
    Proposed for version 2.9
Gather statistics about toolhead communication.

   Payload (5 bytes)
    uint32: Number of packets received from the USB interface
   uint32: Number of packets sent over the RS485 interface
   uint32: Number of packets sent over the RS485 interface that were not responded to
   uint32: Number of packet retries attempted
   uint32: Number of bytes received over the RS485 interface that were discarded as noise

# Buffered Commands
# 128 - RESERVED (Obsolete command)
# 129 - Queue point
    This queues an absolute point to move to.  This may make it easier to implement the host software, but it is much larger than the incremental points which will reduce your available command buffer size.

    Payload (16 bytes)
    int32: x coordinate (units are steps)
    int32: y coordinate (units are steps)
    int32: z coordinate (units are steps)
    uint32: dda speed (in microseconds between steps on the max delta)
# 130 - Set Position
    This command defines the current position of the toolhead as the given position. Ordinarily this is used to set a "home" position.

    Payload (12 bytes)
    int32: x position, in steps
int32: y position, in steps
int32: z position, in steps
# 131 - Find Axes Minimums - Blocking seek to hardware min switches, w/ timeout
    This function will find the hardware minimum. It will home all axes at the same time, so it is up to the host software to generate two separate homing commands if you want to home the Z axis separately.

    Payload (7 bytes)
    uint8: axes flags, where bits 4-0 represent which axes to home: | N/A | N/A | N/A | B | A | Z | Y | X |
    uint32: feedrate (in microseconds between steps) (max 71.58 minutes)
    uint16: timeout (in seconds before abort)  (max = 18 hours) (default = 5 minutes)
# 132 - Find Axes Maximums - Blocking seek to hardware max switches w/ timeout
    This function will find the hardware maximum, or position overflow (2^32), whichever is first.
It should also record this to the eeprom for future use.  This function fill move all axes simulataneously, so it is important to generate two separate commands if you want to seek the Z axis separately.

    Payload (7 bytes)
    uint8: axes flags, where bits 4-0 represent which axes to home: | N/A | N/A | N/A | B | A | Z | Y | X |
    uint32: feedrate (in microseconds between steps) (max 71.58 minutes)
    uint16: timeout (in seconds before abort)  (max = 18 hours) (default = ??)
# 133 - Delay - Simply stop and wait.
    Exactly what it says.

    Payload (4 bytes)
   uint32: delay period (in microseconds) (max 71.58 minutes)
# 134 - Change Tool - Switch to a new tool
    This will trigger a tool change.  If the firmware supports automated tool changing, it will initiate its tool-changing routine.  If it doesn't, it simply updates its currently selected tool and moves on.

    Payload (1 byte)
    uint8: index/address of the desired tool to select
# 135 - Wait For Tool Ready - Wait until a tool is ready before proceeding
    This command is used to tell the machine to wait (for example for the extruder to heat up, etc.)  It will poll the device with the 'are you ready' command until it responds affirmative

    Payload (5 bytes)
    uint8: the index of the tool to wait for before printing.
    uint16: the delay between query packets sent to the tool head in milliseconds (default: 100 milliseconds)
    uint16: the timeout before continuing without tool ready in seconds (default: 1 minute)
# 136 - Tool Action Command - Send an action command to a tool for execution
    This command is for sending an action to the command.  The master firmware will then pass the query along to the appropriate tool, as well as passing the response back as well.

    Payload (3 + N bytes)
    uint8: the index of the tool to query
    uint8: the command for the tool.
    uint8: the length of the command payload (N)
    N bytes: command specific payload, variable size.
# 137 - Enable/Disable Axes - Explicitly power or depower steppers
    This command is used to explicitly power steppers on or off.  Generally, it is used to shut down the steppers after a build to save power and avoid generating excessive heat.

    Payload (1 byte)
    uint8: bitfield
    bit 7: 1 to enable, 0 to disable
    bit 6,5: ignored
       bit 4: Axis 4 (B axis) on
       bit 3: Axis 3 (A axis) on
       bit 2: Axis 2 (Z axis) on
    bit 1: Axis 1 (Y axis) on
    bit 0: Axis 0 (X axis) on

# 138 - User Block
This command will halt further processing of the command queue until the block is cleared by user intervention.  The "Proceed" command will release the block.  This is not equivalent to a pause-- if you want to perform any toolhead operations, like stopping extrusion, you need to do so in a seperate command prior.

Payload (2 bytes):
    uint16: Block identifier.

# 139 - Queue extended point
    This queues an absolute point to move to.  This may make it easier to implement the host software, but it is much larger than the incremental points which will reduce your available command buffer size. This is the 5D equivalent of 129 - Queue Point.

    Payload (24 bytes)
    int32: x coordinate (units are steps)
    int32: y coordinate (units are steps)
    int32: z coordinate (units are steps)
    int32: a coordinate (units are steps)
    int32: b coordinate (units are steps)
    uint32: dda speed (in microseconds between steps on the max delta)
# 140 - Set Extended Position
    This command defines the current position of the toolhead as the given position. Ordinarily this is used to set a "home" position. This is the 5D equivalent of 130 - Set Position.

    Payload (12 bytes)
    int32: x position, in steps
int32: y position, in steps
int32: z position, in steps
    int32: a position, in steps
    int32: b position, in steps
# 141 - Wait For Platform Ready - Wait until the build platform is ready before proceeding
New in version 2.4
    This command is used to tell the machine to wait until the build platform is ready (target temperature has been reached). It will poll the device with the 'are you ready' command until it responds affirmative.

    Payload (5 bytes)
    uint8: the index of the tool to which the build platform is attached
    uint16: the delay between query packets sent to the tool head in milliseconds (default: 100 milliseconds)
    uint16: the timeout before continuing without tool ready in seconds (default: 1 minute)

# 142 - Queue extended point, new style
    New in version 2.7
    This queues a point to move to.  It differs from old-style point queues (see command 139 et. al.) in that it no longer uses the DDA abstraction and instead specifies the total move time in microseconds.  Additionally, each axis can be specified as relative or absolute.  If the "relative" bit is set on an axis, then the motion is considered to be relative; otherwise, it is absolute.

    Payload (25 bytes)
    int32: x coordinate (units are steps)
    int32: y coordinate (units are steps)
    int32: z coordinate (units are steps)
    int32: a coordinate (units are steps)
    int32: b coordinate (units are steps)
    uint32: duration of movement in microseconds
    uint8: relative or absolute motion
    bit 7,6,5: ignored
       bit 4: Axis 4 (B axis) relative
       bit 3: Axis 3 (A axis) relative
       bit 2: Axis 2 (Z axis) relative
    bit 1: Axis 1 (Y axis) relative
    bit 0: Axis 0 (X axis) relative

# 143 - Store Home Positions
    New in version 2.8
    Record the current axes positions to EEPROM.
    Payload (1 byte)
       uint8: As below:

Bit	7	6	5	4	3	2	1	0
Name	N/A	N/A	N/A	B	A	Z	Y	X

# 144 - Recall Home Positions
    New in version 2.8
    Recall the axes positions stored in EEPROM.
    Payload (1 byte)
       uint8: As below:

Bit	7	6	5	4	3	2	1	0
Name	N/A	N/A	N/A	B	A	Z	Y	X

145 – Set Digital Stepper Potentiometer Value
    New in version 3.2; Mighty Board only
    This command will set the value of the digital pototentiometer associated with a stepper motor. The digital potentiometer sets the reference voltage input for the stepper driver. Lower values will result in less current available to the motor. The potentiometers can set VREF from 0-1.7V.
    Payload (2 bytes)
    uint8: the stepper identifier. This value should be in the rang 0-4. 0 is X, 1 is Y, 2 is Z, 3 is A, 4 is B.
    uint8: The value to set the digital potentiometer to. This value should be in the range 0-127. 0 is the lowest value; 127 the highest.

146 – Set RGB LED values
    New in version 3.2; Mighty Board only
    This command will set the brightness of the RGB LEDs in the bot.
    Payload (3 bytes)
    uint8: the R value. 0 turns the R channel off; 255 turns it fully on.
    uint8: the G value. 0 turns the G channel off; 255 turns it fully on.
    uint8: the B value. 0 turns the B channel off; 255 turns it fully on.

147 – Beep
    New in version 3.2; Mighty Board only
    This command will emit a beep from the piezo speaker.
    Payload (4 bytes)
    uint16: the frequency of the beep in Hz.
    uint16: the length of the beep in ms.

148 – Pause for Button
    New in version 4.02; Mighty Board only
    This command will pause the bot for user interaction, ie pressing a button. When a button is pressed the commands continue.
    Payload (4 bytes)
    uint8: Mask of which buttons to accept. As of V 4.02 0xFF (any) is the only valid value
    uint16: seconds to wait for interaction.
    uint8: 1 for 'reset on timeout, 0 for 'do not reset on timeout'.

149 – Display Message
    New in version 4.02; Mighty Board only
    This command will display a message to the bot's onboard user interface, for informational or interface values. Often used with 148 to send info to the bot to get user interaction. NOTE: for word-wrapping of long , line wrap order is 0,2,1,3. Don't ask, it's complicated.
    Payload (4 bytes min)
    uint8: Options, must be 0 for ver 4.02
    uint8: Starting X coordinate for display.
    uint8: Starting Y coordinate for display.
    uint8: display timeout in seconds. After timeout display returns to previous state/information.
    uint8: (up to 25) string of characters to display, null terminated.

150 – Set Build Percentage
    New in version 4.03; Mighty Board only
    This command will manually override the the build complete % on the bot, overriding the existing build complete %. This will override build % for SD card events, and/or from the bot.
    Payload (2 bytes)
    uint8: the new build % in the range 0 – 100.
    uint8: Reserved byte for future use

151 – Queue onboard song
    New in version 4.03; Mighty Board only
    This command will flag the bot to play a built-in song. Default songs are Error Sound (0), a Ta-da sound (1), and a warning sound (2). All other sounds are user or machine specific, with the warning song (2) the default for unknown sounds.
    Payload (2 bytes)
    uint8: The song ID to play.
    uint8: Reserved byte for future use

152 – Reset to factory settings
    New in version 4.03; Mighty Board only
    This command will reset the motherboard to factory settings.
    Payload (1 bytes)
    uint8: reserved for future use. 0xFF expected.

# Slave Microcontroller Commands (Extruder)
# Query Commands
# 0 - Get Version
    This command allows the master and slave to exchange version numbers.  It also allows for simple automated discovery of the firmware.  Version numbers will always be stored as a single number, Arduino / Processing style.  Thus, the versions will be 0 to 65535.

    Payload (2 bytes) - host version
    uint16: Host Version

Response (2 bytes) - firmware version
    uint16: Firmware Version
# 1 - Init - Initialize firmware to boot state
    Initialization consists of:
  - setting desired temperature to zero
  - turning off all devices (fan, coolant, etc.)
  - detaching all servo devices
  - setting desired RPM / PWM to zero

    Payload (0 bytes)
    Response (0 bytes)
# 2 - Get Temperature
    This returns the last recorded temperature.  It's important for speed purposes that it does not actually trigger a temperature reading, but rather returns the last reading.  The slave firmware should be constantly monitoring its temperature and keeping track of the latest readings.

    Payload (0 bytes)

    Response (2 bytes)
   int16: Current Temperature in Celsius
# 3 - Set Target Temperature
    This sets the desired temperature for the heating element.  The slave firmware will then attempt to maintain this temperature as closely as possible.

    Payload (2 bytes)
  int16: Desired Target Temperature in Celsius
# 4 - Set Motor 1 Speed (PWM)
    This sets the motor speed as a PWM value.  Motor 1 generally corresponds to the extruder motor (M101-M103, M108 GCodes). It should not actually enable the motor until the motor enable command is given.

    Payload (1 byte)
    uint8: Desired PWM speed
# 5 - Set Motor 2 Speed (PWM)
    This sets the motor speed as a PWM value.  Motor 2 generally corresponds to the spindle motor (??? GCodes). It should not actually enable the motor until the motor enable command is given.

    Payload (1 byte)
    uint8: Desired PWM speed
# 6 - Set Motor 1 Speed (RPM)
    This sets the motor speed as an RPM value.  Motor 1 generally corresponds to the spindle motor (M101-M103, M108 GCodes). It should not actually enable the motor until the motor enable command is given.  For this command to actually work, a quadrature encoder, or tachometer must actually be attached to the motor.

    Payload (4 bytes)
    uint32: speed in microseconds between complete rotations.
# 7 - Set Motor 2 Speed (RPM)
    This sets the motor speed as an RPM value.  Motor 1 generally corresponds to the spindle motor (??? GCodes). It should not actually enable the motor until the motor enable command is given.  For this command to actually work, a quadrature encoder, or tachometer must actually be attached to the motor.

    Payload (4 bytes)
    uint32: speed in microseconds between complete rotations.
# 8 - Set Motor 1 Direction
    This sets the desired rotation direction of the motor.  It does not turn the motor on or off.

    Payload (1 byte)
   uint8: 0 = reverse / counter clockwise, 1 = forward / clockwise
# 9 - Set Motor 2 Direction
    This sets the desired rotation direction of the motor.  It does not turn the motor on or off.

    Payload (1 byte)
    uint8: 0 = reverse / counter clockwise, 1 = forward / clockwise
# 10 - Toggle Motor 1 (on/off)
    This turns the motor on or off.  It is possible to also set the direction of the motor as well.  This makes the command fairly efficient, since you can turn the motor on while setting the direction as well.  When the motor is enabled, it will move at the previously specified speed (either RPM or PWM).

    Payload (1 byte)
    uint8: The bottom two bits of this command determine direction and enable status:

Bit	7	6	5	4	3	2	1	0
Name	N/A	N/A	N/A	N/A	N/A	N/A	DIR	ENABLE

ENABLE - HIGH means motor is enabled, LOW means motor is disabled.
DIR - HIGH means motor rotates Clockwise, LOW means motor rotates Counter Clockwise
# 11 - Toggle Motor 2 (on/off)
    This turns the motor on or off.  It is possible to also set the direction of the motor as well.  This makes the command fairly efficient, since you can turn the motor on while setting the direction as well.  When the motor is enabled, it will move at the previously specified speed (either RPM or PWM).

    Payload (1 byte)
    uint8: The bottom two bits of this command determine direction and enable status:

Bit	7	6	5	4	3	2	1	0
Name	N/A	N/A	N/A	N/A	N/A	N/A	DIR	ENABLE

ENABLE - HIGH means motor is enabled, LOW means motor is disabled.
DIR - HIGH means motor rotates Clockwise, LOW means motor rotates Counter Clockwise
# 12 - Toggle Fan (on/off)
    This turns the fan, or the output connected to the fan output on or off.

    Payload (1 byte)
    uint8: The bottom bit of this command determine enable status:

Bit	7	6	5	4	3	2	1	0
Name	N/A	N/A	N/A	N/A	N/A	N/A	N/A	ENABLE

ENABLE - HIGH means fan is enabled, LOW means fan is disabled.
# 13 - Toggle Valve (on/off)
    This opens the valve, or the output connected to the valve output on or off.

Payload (1 byte)
    uint8: The bottom bit of this command determine enable status:

Bit	7	6	5	4	3	2	1	0
Name	N/A	N/A	N/A	N/A	N/A	N/A	N/A	ENABLE

ENABLE - HIGH means valve is enabled (open), LOW means valve is disabled (closed).
# 14 - Set Servo 1 Position
    This is basically just a wrapper to the Arduino hardware Servo library on pins 9 & 10.  It supports full servo angles, and can also do continuous rotation: http://arduino.cc/en/Reference/Servo

    Payload (1 byte)
    uint8: desired angle (from 0 to 180)
# 15 - Set Servo 2 Position
    This is basically just a wrapper to the Arduino hardware Servo library on pins 9 & 10.  It supports full servo angles, and can also do continuous rotation: http://arduino.cc/en/Reference/Servo

    Payload (1 byte)
    uint8: desired angle (from 0 to 180)
# 16 - Filament Status
    Payload (0 bytes)

    Response (1 byte)
   uint8: status: 0 - empty, 255 = full, number between 0-255 represents percentage of filament remaining.
# 17 - Get Motor 1 Speed (RPM)
    Payload (0 bytes)

    Response
    uint32: speed in microseconds between complete rotations.
# 18 - Get Motor 2 Speed (RPM)
    Payload (0 bytes)

    Response
    uint32: speed in microseconds between complete rotations.
# 19 - Get Motor 1 Speed (PWM)
    Payload (0 bytes)

    Response (1 byte)
    uint8: current PWM value for the motor.
# 20 - Get Motor 2 Speed (PWM)
    Payload (0 bytes)

    Response (1 byte)
    uint8: current PWM value for the motor.
# 21 - Select Tool
    Tell a tool that it has been selected as the default tool.  The tool may or may not choose to do anything with that information.

Payload (0 bytes)
Response (0 bytes)
# 22 - Is Tool Ready?
    Asks the tool if it is ready to be used.  Examples of ready states might be: spindle up to speed, temperature at target, etc.

    Payload (0 bytes)
    Response (1 byte)
    uint8: 0 for not ready, 1 for ready.
# 23 - Pause/Unpause - Halt Execution Temporarily
    Behaves in a similar fashion to the pause/unpause functionality of the motherboard.

    Payload (0 bytes)
Response (0 bytes)
# 24 - Abort - Terminate all operations and reset
    Behaves in a similar fashion to the abort functionality of the motherboard.

    Payload (0 bytes)
Response (0 bytes)
# 25 - Read from EEPROM
    Read the specified number of bytes from the given offset in the EEPROM and return it in the response packet.  The maximum read size is 32 bytes.

    Payload (3 bytes)
    uint16: the offset of the read
    uint8: the number of bytes to return, N.  N <= 16.

    Response (N bytes)
    N bytes: the data read from the EEPROM.
# 26 - Write to EEPROM
    Write the given bytes to the EEPROM starting at the specified location.  The maximum payload size is 16 bytes.  WARNING: this operation can be potentially slow (about 3.3ms * N) and will block all other operations.  It's not recommended to write to the EEPROM while a build is in progress.

    Payload (3+N bytes)
    uint16: the offset of the write
    uint8: the length of the data
    N bytes: the data to write

    Response (1 byte)
    uint8: the number of bytes successfully written.

# 30 - Get Build Platform Temperature
    This returns the last recorded temperature of the build platform.  It's does not actually trigger a temperature reading, but rather returns the last reading.  The slave firmware should be regularly monitoring its temperature and keeping track of the latest readings.

    Payload (0 bytes)

    Response (2 bytes)
   int16: Current build platform temperature, in Celsius.
# 31 - Set Build Platform Target Temperature
    This sets the desired temperature for the build platform element.  The slave firmware will then attempt to maintain this temperature as closely as possible.

    Payload (2 bytes)
  int16: Desired build platform temperature, in Celsius.

# 32 - Get Extruder Target Temperature
    New in v2.3 firmware
    This command retrieves the last temperature set for the extruder.

    Payload (0 bytes)

    Response (2 bytes)
   int16: The last set extruder temperature, in Celsius.

# 33 - Get Build Platform Target Temperature
    New in v2.3 firmware
    This command retrieves the last temperature set for the build platform.

    Payload (0 bytes)

    Response (2 bytes)
   int16: The last set build platform temperature, in Celsius.

# 34 - Get firmware build name
    New in version 2.5
    Retrieve the firmware build name, which is a human-readable string describing the build.  Names should be chosen with an eye towards disambiguating builds targeted for different tools.
    Payload length limitations restrict this field to 31 characters.
    Payload (0 bytes)
    Response (N+1)
    char[N+1]: a null-terminated string representing the build name

# 35 - Is Build Platform Ready?
New in version 2.6
Asks the heated build platform if it is ready to be used, typically waits for temperature to be reached.

    Payload (0 bytes)
    Response (1 byte)
    uint8: 0 for not ready, 1 for ready.
# 36 - Get Tool Status
    New in version 2.7
    Retrieve some information about the current tool

    Payload (0 bytes)
    Response (1 byte)
       uint8: As below:

Bit	7	6	5	4	3	2	1	0
Name	EXTRUDER_ERROR	PLATFORM_ERROR	WDRF	BORF	EXTRF	PORF	N/A	EXTRUDER_READY

EXTRUDER_ERROR - HIGH means an error was detected with the extruder heater (if the tool supports one), LOW means it is fine. The extruder heater will fail if an error is detected with the sensor (thermocouple) or if the temperature reading appears to be unreasonable.
PLATFORM_ERROR - HIGH means an error was detected with the platform heater (if the tool supports one), LOW means it is fine. The platform heater will fail if an error is detected with the sensor (thermocouple) or if the temperature reading appears to be unreasonable.
WDRF - Watchdog reset flag was set at restart
BORF - Brown out reset flag was set at restart
EXTRF - External reset flag was set at restart
PORF - Power-on reset flag was set at restart
EXTRUDER_READY - HIGH means extruder has reached target temperature, LOW means it has not.
# 37 - Get PID state
    New in version 2.7
    Retrieve the state variables of the PID controller. This is intended for tuning the PID constants.

    Payload (0 bytes)
    Response (12 bytes)
    int16: Extruder heater error term
    int16: Extruder heater delta term
    int16: Extruder heater last output
    int16: Platform heater error term
    int16: Platform heater delta term
    int16: Platform heater last output

# 38 - Set Motor 1 Speed (DDA)
Proposed for 2.8 (RG)
This sets the stepper motor speed as a DDA value, or microseconds between steps. It should not actually enable the motor until the motor enable command is given. For future implementation of 5D (vs 4D) two DDA codes are sent - the DDA to start with and the DDA to end with. The third uint32 is the number of steps to take. The direction to go is set by code 8 - Set Motor 1 Direction.

    Payload (12 bytes)
uint32: speed in microseconds between steps (start of movement).

uint32: speed in microseconds between steps (end of movement).
uint32: total steps to take.

# 39 - Set Motor 2 Speed (DDA)
Proposed for 2.8 (RG)

This sets the stepper motor speed as a DDA value, or microseconds between steps. It should not actually enable the motor until the motor enable command is given. For future implementation of 5D (vs 4D) two DDA codes are sent - the DDA to start with and the DDA to end with. The third uint32 is the number of steps to take. The direction to go is set by code 9 - Set Motor 2 Direction.

Payload (12 bytes)
uint32: speed in microseconds between steps (start of movement).
uint32: speed in microseconds between steps (end of movement).
uint32: total steps to take.

# 40 - Light indicator LED
   Proposed for 2.9
    This command turns on an indicator light (for gen 4, the motor direction LED). This command is intended to serve as visual feedback to an operator that the electronics are communicating properly. Note that it should not be used during regular operation, because it interferes with h-bridge operation.

# Changes and additions to the protocol
2011-6-20 This section was quite out of date, and has been removed.
# Errata

Homing. There appears to be multiple approaches to homing. I'll explain ours. If you do the same or know about other common approaches, we should find a good solution (MK):
  1. When starting a print, we first home to hardware switches. The firmware knows in which direction to home; it will home in the negative direction in X/Y and in positive direction in Z. Positive Z means at it's maximum height about the base plane. Homing is done with a fast feedrate until the optical switches hit. Then we'll reverse direction and move very slowly until the optical switches are clear again. This will give us a very accurate absolute reference position. ZH: Yes, this is exactly what the homing command will do.pushd
MK: We don't yet have a "homing command", only "find axes min/max". Idea: We could create a new command, "Goto Reference", which will home to the defined reference position (which may be a combination of min and max for the three axes). The find axes min/max would then only be needed to record the working area (range), and could then be joined into a separate command (Find Range). The range could of course be (partially) hardcoded into the firmware if the necessary switches are not present. Find Range would take a while to execute, but that's ok. We could even save the current range in EEPROM.  ZH: I'd really like to keep the firmware as simple as possible, and move this type of complicated zero-point initialization into the host side of things.  Really, all we're talking about here is something that could easily be represented as a series of commands (range: find min x/y/z, find max x/y/z, get range)  or (goto reference: home xyz, goto X, Y, Z)  additionally, the logic on these types of things is something that could change from machine to machine, and people will want to experiment with themselves.  putting it on the host means we're much more flexible (ie: we could have a <reference> block of gcode that is user-editable for setting reference points.
MK: I'm still leaning towards putting more of this in firmware. The firmware still needs to be configured somehow (pin mapping, supported features, endstop positions, axis layoutt; which direction is positive vs. negative), and I think the reference configuration belongs together with this and not in run-time configuration sent from the host. We could make all this configurable over serial and store the configuration in EEPROM. It's a bit scary though (it's to easy to destroy hardware with software if someone presses the wrong button). I suggest that we investigate this by testing out different approaches in practice on our respective hardware setups by supporting multiple approaches in the initial phases and discuss this further later on.
agm: I really like the idea of storing the range in EEPROM.  We could have a retrieve range that returns null if it has not been set yet, and a calibrate command that would find and store the range.  (A subsequent retrieve would get the updated data.)
- Now, we'll move to the logical origin. This is configured on the host side since it needs to be calibrated every time we change the extruder head or exchange the printing base plate. In the future, this position would change for each model in a batch print. This will move the extruder head so that it touches the base plate (depending on local experience). In the future, this calibration could be automated by probing for the Z depth (e.g. using a piezo sensor embedded into the base plate, or a simple contact exploiting that the extruder head is conductive and grounding it). ZH: This can be accomplished by queuing an absolute point after it has homed to hardware switches. MK: Exactly.
- Set the current position to (0, 0, 0). This is what the g-code file expects; the local origin of the object currently being printed. For future batch printing, we should probably reset this for each object, after repeating ZH: This can/should also be accomplished by sending a 'set position' command after the previous two steps complete. MK: Yeps. agm: is there any reason for the hardware to know or care what the local zero is?  Why not just have the driver feed it commands relative to the absolute limit-switch zero? MK: True enough. The logic for handling this will be on the host side, as well as any batching support. One thing we should think about though: How do we integrate this with the SD-card, LCD panel and autonomous printing ideas? Let's make this a separate section.
- From our machines.xml:  ZH: This will work exactly as it has before... the joy of a driver-based system that understands gcode at a high level. MK: Perfect
- <warmup>
    M103 (extruder off)
    G90 (abs)
    G30 X0 Y0 Z0 F780
    M104 S215.0 (heat)
    G0 X120.00 Y110.00 Z-104.50 F780
    G92 (Metalab define current as home)
  </warmup>
  <cooldown>
    G91 (Metalab relative positioning)
    G1 Z10 F780 (move up)
  </cooldown>